## Slide 1
What is the construction date for affected areas
PCB Containing Building Materials Management
Renovation
Demolition
If materials are between 4 and 49 ppm dispose as Residual Waste in PA landfill. (Same if material also contains ACM)
If materials are
> 50 ppm
Sample adjacent substrate.
Sample surrounding soil, asphalt, concrete, etc.
Sample all caulk and glazing putties
See waste chart for disposal options
Sample only those materials affected
1980 or newer
No further action
Pre 1980 Construction
Will adjacent substrate be removed?
If No, See Section 1 in waste chart for disposal options
If Yes, see Section 2 in waste chart for disposal options
If materials are
> 50 ppm
If materials are between 4 and 49 ppm dispose as Residual Waste in PA landfill (Same if material also contains ACM)
If materials are
< 4 ppm no further action
Façade Washing
If existing building materials are known to contain PCB’s > 50 ppm water must be captured for sampling and proper disposal/treatment.
If no data exists a test wash must be performed, and water sampled to determine if capture is required.
If materials are
< 4 ppm no further action
Notes: PCB Containing Building Materials Management
What is the construction date for affected areas?
If 1980 or newer, then no further action is needed.
If Pre 1980 Construction.
  Demolition
    Sample all the caulk and glazing putties.
      If materials are ≤4 ppm no further action.
      If materials are between 4 and 49 ppm dispose as Residual Waste in PA landfill. (Same if material also contains ACM).
      If materials are ≥50 ppm.
        Sample adjacent substrate. Sample surrounding soil, asphalt, concrete, etc.
        See waste chart for disposal options.
  Renovation
    Sample only those materials affected.
      If materials are ≤4 ppm no further action.
      If materials are between 4 and 49 ppm dispose as Residual Waste in PA landfill (Same if material also contains ACM).
      If materials are ≥50 ppm.
      Will adjacent substrate be removed?
        If No, See Section 1 (slide 2) in waste chart for disposal options.
        If Yes, see Section 2 (slide 3) in waste chart for disposal options.
  Façade Washing
    If existing building materials are known to contain PCB’s ≥50 ppm water must be captured for sampling and proper disposal/treatment.
    If no data exists a test wash must be performed, and water sampled to determine if capture is required.

## Slide 2
PCB Waste Disposal – Section 1
Caulk and/or Glazing Putties ONLY
If materials are between 4 and 49 ppm dispose as Residual Waste in PA landfill (Same if material also contains ACM)
PCB Only – EHS disposal as PCB Bulk Product in PA Sub-Title D Landfill that accepts > 50 ppm PCB waste
(TCLP Sampling and PA DEP approval needed)
If materials are > 50 ppm
Façade Washing
If wash water contains PCB’s < 1 ppm dispose in pre-designated sanitary drain
If wash water contains PCB’s > 1 ppm but < 50 ppm, EHS to dispose with contracted waste vendor for treatment.
If wash water contains PCB’s > 50 ppm, EHS to dispose with contracted waste vendor and must go to an incinerator as hazardous waste.
PCB and Asbestos – EHS Disposal as a TSCA waste at a Sub-Title C Landfill
If materials are
< 4 ppm no further action
Notes: PCB Waste Disposal – Section 1
Caulk and/or Glazing Putties ONLY
If materials are ≤ 4 ppm no further action.
If materials are between 4 and 49 ppm dispose as Residual Waste in PA landfill (Same if material also contains ACM).
If materials are ≥ 50 ppm.
  PCB and Asbestos–EHS Disposal as a TSCA waste at a Sub-Title C Landfill.
  PCB Only–EHS disposal as PCB Bulk Product in PA Sub-Title D Landfill that accepts > 50 ppm PCB waste (TCLP Sampling and PA DEP approval needed).
Façade Washing
If wash water contains PCB’s ≤ 1 ppm dispose in pre-designated sanitary drain.
If wash water contains PCB’s > 1 ppm but < 50 ppm, EHS to dispose with contracted waste vendor for treatment.
If wash water contains PCB’s ≥ 50 ppm, EHS to dispose with contracted waste vendor and must go to an incinerator as hazardous waste.

## Slide 3
Caulk and/or Glazing Putties
(> 50 ppm) and Contaminated Substrate, Soil, Asphalt, Concrete, etc.
PCB Waste Disposal – Section 2
Source Material Caulk/Glazing (Original) including substrate. EHS disposal as PCB Bulk Product in PA Sub-Title D Landfill that accepts > 50 ppm PCB waste
(DEP approval needed)
If material also contains ACM – EHS Disposal as a TSCA waste at a Sub-Title C Landfill
Non-Source Material: Remediation Waste
Replacement caulk > 1 ppm
Contaminated substrate > 1 ppm
Contaminated Soil, Asphalt, Concrete, etc. > 1 ppm
LARGE VOLUME OPTION
If material is < 50 ppm PCB an EPA Risk Based Remediation Plan can be submitted to EPA to request disposal as a Non-TSCA waste at a PA Sub-Title D Landfill
If material is > 50 ppm PCB
EHS Disposal as a TSCA waste at Sub-Title C Landfill
SMALL VOLUME OPTION
If material is < 50 ppm PCB EHS Disposal as a TSCA waste at a Sub-Title C Landfill
(No EPA approval needed)
Notes: PCB Waste Disposal – Section 2
Caulk and/or Glazing Putties (≥50 ppm) and Contaminated Substrate, Soil, Asphalt, Concrete, etc.
Source Material Caulk/Glazing (Original) including substrate. EHS disposal as PCB Bulk Product in PA Sub-Title D Landfill that accepts ≥50 ppm PCB waste (DEP Approval needed).
  If material also contains ACM – EHS Disposal as a TSCA waste at a Sub-Title C Landfill.
Non-Source Material: Remediation Waste
  Replacement caulk >1 ppm.
  Contaminated substrate >1 ppm.
  Contaminated Soil, Asphalt, Concrete, etc. >1 ppm.
    SMALL VOLUME OPTION—if material is < 50 ppm PCB EHS Disposal as a TSCA waste at a Sub-Title C Landfill (No EPA approval needed).
    LARGE VOLUME OPTION—if material is < 50 ppm PCB an EPA Risk Based Remediation Plan can be submitted to EPA to request disposal as a Non-TSCA waste at a PA Sub-Title D Landfill.
    If material is ≥50 ppm PCB EHS Disposal as a TSCA waste at Sub-Title C Landfill.