# 1.0 Purpose and Requirements

This guide will present a summary of the basics of radiofrequency (RF) and microwave safety, biological effects, and exposure limits to be used at Penn State University. Some recommendations are made that, if followed, would enhance the safety of equipment. In other cases a particular item or action will be required.

Questions or comments concerning this guide may be sent to Yuanqing Guo at yxg14@psu.edu.

## 2.0 Scope and Regulations

This guide applies to all users of devices and equipment designed to generate RF and/or microwave fields. Examples include radar, telecommunications transmitters, cell phone transmitters, RF heat sealers, and microwave heating equipment.

Of particular note, consumer grade microwave ovens are not included in this guide as they must meet stringent federal safety requirements. EH&S will survey ovens upon request.

2.1 General Federal Regulations

RF and microwave exposure limits are promulgated by the Federal Communication Commission (FCC) and the Occupational Health and Safety Administration (OSHA). In some cases regulations contradict each other (due to differences in emphasis or older data). In these cases the more conservative FCC or OSHA limit will be used.

In general, PSU will follow FCC limits, see Section 5.0.

2.2 FCC Requirements

Currently the FCC has adopted exposure limits from the National Council on Radiation Protection (NCRP) and can be found in the federal regulations at 47 CFR 1.1307(b), 1.1310, 2.1091, 2.1093, and at http://www.fcc.gov/oet/rfsafety/rf-faqs.html. The FCC recommendations covers 300 kHz to 100 GHz and tables of FCC limits can be found at http://www.fcc.gov/oet/info/documents/bulletins/#56 . See Figure 1 in this guide.

2.3  OSHA Regulations

OSHA requirements can be found in 29 CFR 1910.97 and covers the range of 10 MHz to 100 GHz. The link for OSHA limits is http://www.osha.gov/pls/oshaweb/owadisp.show_document?p_table=STANDARDS&p_id=9745. See Figure 2 in this guide.

2.4 IEEE/ANSI Standard

The American National Standards Institute (ANSI) publishes recommended limits in standard number IEEE/ANSI C95.1-2005 and covers the range of 100 kHz to 100 GHz. See Figure 3 in this guide.

2.5 ICNIRP Recommendations

The International Commission on Non-Ionizing Radiation Protection (ICNIRP) has issued guidelines for exposures from 100 kHz to 300 GHz in Guidelines for Limiting Exposure to Time-Varying Electric, Magnetic, and Electromagnetic Fields, 1998 (ICNIRP 1998). See Figure 4 in this guide.

2.6 ACGIH TLVs

The American Conference of Governmental Industrial Hygienists publishes Threshold Limit Values for chemical and physical agents. The 2008 TLV values for RF and microwaves is shown in Figure 5 in this guide.

2.7 All Limits and Guidelines Comparison

Figure 6 shows some of the major limits and guidelines on one graph for comparison purposes.

# 3.0 Definitions

- Specific Absorption Rate (SAR)
The power absorbed by a body when exposed to electromagnetic radiation. The current SAR limit is 4 watts/kg (4 W/kg). To be conservative, standards setting organizations use 1/10 of this value.

- Power Density
Power per unit area, typically milliwatts/cm2 or watts/m2.

- Near Field
The region close to the RF emitter (i.e. antenna) where the electric and magnetic fields are not perpendicular to each other, and their orientation varies from point to point. The near field extends a distance less than one wavelength from the emitter. Power density measurements are not useful and often not possible in the near field.

- Far Field
Region where the electric and magnetic fields are perpendicular to each other, and do not vary from point to point. Power density measurements are possible in the far field.

- ISM Bands
Frequencies designated for industrial, scientific, and medical (ISM) use where radiated power is not regulated. Some typical ISM frequencies are 3.56 MHz, 27.12 MHz, 9.5 MHz, 2450 MHz, and 5800 MHz. Because emitted power is not regulated, safety hazards may be created due to high radiated power.

- E Field
Electric field strength component of RF energy measured in volt/meter (V/m).

- H field
Magnetic field strength component of RF energy measured in amps/meter (A/m).

# 4.0 Biological Effects

4.1    General Thermal Effects

The most pronounced biological effect from RF and microwaves radiation is heating, or thermal changes in the body. In its interaction with matter, RF energy may be reflected (as in the case of metals), transmitted through a medium (such as glass) with little energy loss, or be absorbed raising the temperature of the absorber. This increase in temperature can be attributed to two effects. Joule heating is due to ionic currents induced by the electric fields that are set up in the absorber. These ionic currents cause electrons to collide with molecules in tissue and resistance heating results. The other effect is due to the interaction between polar molecules in the absorber and high frequency electric fields. The polar molecules begin to oscillate back and forth in an attempt to maintain proper alignment with the electric field. These oscillations are resisted by other forces and this vibratory resistance is converted into heat.

Absorption of RF radiation and thus heating of the body tissues depends on several factors including wavelength and wave front characteristics. Frequencies greater than 10,000 MHz (10 GHz) are absorbed mostly in the outer skin.

Frequencies between 10,000 MHz and 2500 MHz penetrate more deeply (3 mm to 2 cm) and at wavelengths of 2500 MHz to 1300 MHz, penetration and absorption are sufficient enough to cause damage to internal organs by tissue heating. Therefore the absorption and penetration depth of RF and microwaves in tissue appear to be inverse functions of frequency. See Figure 7.

Heat absorption will be greatest in tissues that have high water content, such as muscle, with less heat absorption taking place in bone and fat.

In the past most biological effects have been related to the incident power density (mW/cm2). However, the absorption of electromagnetic energy is strongly dependant on its frequency, the geometry of the exposure situation and the dielectric properties of the tissue. Because of these factors, biological effects are more properly related to the absorbed energy defined as the specific absorption rate or SAR.

After reviewing a large body of biological data, several standards setting organizations (e.g. ACGIH, IEEE/ANSI, ICNIRP, FCC, etc.) found that hazardous bio effects in humans occurs at a whole body SAR exceeding 4 W/kg; to be conservative, standards setting organizations use 1/10 of this value. For comparison purposes, the resting metabolic rate in humans is on the order of 1 W/kg and 5 W/kg when engaging in strenuous activity such as running. The heart’s metabolic rate is 33 W/kg. The effectiveness of the circulatory system in redistributing thermal energy is dependent upon the degree of vascularization in any tissue, but is generally adequate to cope with varying metabolic rates in the human body.

Blood flow eventually distributes excess heat throughout the body. Sweating starts when the body becomes overheated and cools the body by evaporation. The additional heat load that is imposed on the body due to RF absorption must be dissipated like any other heat load, and can be a significant health concern. Body functions can be impaired when its temperature reaches 102oF and fatal near 107 to 108 oF.

Temperature rise will be greatest in tissues that lack or have poor thermoregulatory mechanisms such as high blood flow. Examples are the eyes and testes. “Hot spots” between tissue interfaces due to non-uniform heating can also develop caused by reflective wave reinforcement.

4.2	Specific Thermal Effects

Ocular Effects

Lens opacification sufficient to cause reduced or loss of vision is termed a cataract. Animal studies have shown that the critical range of frequencies is from 800 to 10,000 MHz.

Damage to the inside layer of the cornea may also occur resulting in corneal damage and loss of sight. This may occur from continuous wave exposure or pulsed exposure, and varying with time in animal studies. See Figure 8.

Auditory Effects

Exposure to pulsed RF or microwave energy may result in hearing a click or buzzing sound originating inside or behind the head. The cause is thought to be a microthermal mechanism, with pressure waves being formed in the middle ear. This effect is thought to be harmless but reports should be treated as possible overexposure.

4.3	Non-thermal Effects

Some animal studies have shown central nervous system effects, altered cell membrane permeability, behavioral effects, and others. These bio effects are attributed to mechanisms other than thermal, and are generally thought to be caused by exposures less than 10 mW/cm2; however, they are not well understood or documented.

Some studies may hint to a link between RF exposure and an increased risk of cancer but this is inconclusive.

4.4	Other Effects

Behavioral

RF/microwave workers complaints have been noted to include nervousness, irritability, headache, depression, sleeplessness, and others.

Immunological

Studies have shown positive immune system effects while other studies have shown suppressed effect. The mechanisms are not well understood or documented.

Depressed Spermatogenesis

Sperm production may be impaired with extended exposures over 10 mW/cm2. This is thought to be reversible after exposure ceases. As sperm production is very sensitive to heat, exposure to RF may understandable produce this effect. In animal studies prolonged exposure or exposure to high RF levels may cause testicular damage, or debilitated or stillborn offspring.

Heat Sensation

Heat sensation may also be the result of over exposure to RF radiation. A documented incident where an RF worker “felt” heat was an exposure of 380 mW/cm2.

# 5.0 RF and Microwave Exposure Limits

For occupational and public exposure limits, PSU will follow the FCC limits shown in Figure 1 since the FCC limits tend to be conservative. For occupational exposures, the field strength is averaged over a 6 min time period. For public exposures the field strength is averaged over at 30 min period.

For frequencies over 100,000 MHz, the 100,000 MHz FCC limits will be extended to 300,000 MHz.

6.0 Electric Shock Hazards

From kHz to 100 MHz, electric shock from induced currents in the free-standing body, or in contact with conductive materials, may be experienced.

# 7.0 Conversions

- 1 W/m2 = 0.1 mW/cm2

- E = electric field strength in V/m

- H = magnetic field strength in A/m

- Power density (PD) = E x H V-A/m2 = watt/m2

- Approximate PD can be found from:
PD = E2 / 3770 mW/cm2	or
PD = 37.7 x H2
Note:  Direct measurement of PD in the near field is difficult and E and H values will change with position, use the maximum E or H values or move further away into the far field region.

- Impedance of free space = 377 ohms

8.0 RF & Microwave Equipment Safety Guidelines

- RF and microwave equipment should be inspected regularly both visually and operationally.

- Visual inspection should include:

  - General safety / housekeeping conditions in the surrounding area

  - Presence and functionality of safety interlocks

  - High voltage safety features (e.g. grounding rods, etc.)

  - Condition of cables and coax lines that transmit RF

  - Presence and condition of RF shielding.

- Operational inspection should include:

  - Monitoring or survey of RF levels, especially in occupied spaces

  - Test of interlocks to inhibit RF generation when tripped

  - Verify proper use of “lockout / tagout” for RF and/or high voltage equipment.

- Engineering controls represent the best approach to RF / microwave safety and the use of shielding can greatly reduce or eliminate exposure.

  - Shields can be solid panels or metallic mesh screening. Materials for shielding E fields include tin, copper, aluminum, silver, and gold. These have high reflective losses for E fields. H field shielding materials include ferrous materials like iron, steel and special alloys (Hypernom and Permalloy for example).

- Mesh screening can provide shielding and visibility and works well for shielding windows and view ports. The size of the mesh is determined by the power, frequency, and wire diameter. A graph for determining the mesh needed is shown in Figure 9.

- Equipment enclosures, access panels, doors, etc. should be sealed with metal braid or other conductive gaskets.

- Grounding straps and wires should not be bent at sharp angles - sharp angles act as antenna to radiate RF. Conductors and straps carrying RF should bend gently and blend smoothly at connection points. Screws used to connect conductors should have smooth, rounded heads, not sharp edged angular heads. Solder connections should be as large in area as possible.

9.0 References

- IRPA Guidelines, Health Physcis, Vol 54 No 1, pp.115-123, 1988.

- IEEE Standard for Safety Levels with Respect to Human Exposure to Radio Frequency Electromagnetic Fields 3 kHz to 300 GHz, IEEE/ANSI, C95.1-2005.

- Heat Stress Due to RF Radiation, Proc of IEEE, Vol 57 No 2, February 1969.

- Biomedical Aspects of Microwave Exposure, AIHA Jour, May, pp. 338-345, 1971.

Figure 1 – FCC Exposure Limits

Figure 2 – OSHA Exposure Guide

Figure 3 – IEEE/ANSI C95.1-2005 Occupational Limits

Figure 3 Continued – IEEE/ANSI C95.1-2005 Public Limits

Figure 4 – ICNIRP Exposure Occupational Guidelines

Figure 4 Continued – ICNIRP Exposure Public Guidelines

Figure 5 – ACGIH TLV Values

Figure 6 – Comparison of All Limits and Guidelines

Figure 7 – Examples of Penetration in Tissue

Figure 8 – Cataract Threshold Power Density

Figure 9 – Graph for Determining the Mesh Size Needed for Shielding